## Slide 1: Learn to Solder
Dallas Makerspace
28 December 2018
Dale Wheat

## Slide 2: Introduction
Goal Introduction to soldering for electronic projects
Time One hour
Format Hands-on
Instructor Dale Wheat
Requirements Desire to learn

## Slide 3: Goals and Expectations
Just enough practice to get started
Learn to use the basic tools safely
Inspire new ideas
Your goals?

## Slide 4: Safety Concerns
Burn hazard
  Soldering irons are hot enough to melt metal
  Causes the kind of pain that lasts for days
Lead is a poison
  We will be using solder that contains lead
  Lead-free solder is available but is more difficult to use
  Wash your hands after handling solder containing lead
Small parts are used
  Wear your good reading glasses, if needed
  Always have good lighting
  Eye protection is available

## Slide 5: Preflight Check
Comfy?
Nervous?
Work area clear?
Tools in reach?
Adequate lighting?
Sponge wet?
Power on!

## Slide 6: Part 1 – Wood Burning
Hold the soldering iron like a pencil in your dominant hand
Never touch the metal parts of the soldering iron
Locate your block of wood
Hold the wood with your non-dominant hand
Use the soldering iron to “draw” on the wood
Show off your (choose one):
  Artistic capabilities
  Hand lettering
  Spelling
Melt some solder

## Slide 7: Part 2 – Practice Makes Perfect
Fill some of the holes with solder
Install the components
Solder the components
Trim the leads
Repeat

## Slide 8: Part 3 – Build the Wee Blinky
Overview
Identify the components
Install shortest components first
Observe component polarity
Test

## Slide 9
1 Page
4 Steps

## Slide 10: Parts Check
(1) Wee Blinky PCB
(2) 1KΩ resistor – brown, black, red stripes
(2) 33KΩ resistor – orange, orange, orange stripes
(2) LEDs
(2) Transistors
(2) Capacitors
(1) 9V battery snap (not pictured)

## Slide 11: Install Resistors
Resistors are NOT polarized
They can be installed in any direction
Install all four resistors at once…
  R1 = 1KΩ
  R2 = 33KΩ
  R3 = 33KΩ
  R4 = 1KΩ
… or install one at a time

## Slide 12: Install Transistors
Cut leads as long as possible
Transistors ARE polarized
Both transistors face the same direction
Refer to part outlines on PCB

## Slide 13: Install LEDs
LEDs ARE polarized
“Long lead, square hole!”
Various possible mountings:
  Flush
  Weird

## Slide 14: Install Capacitors
Capacitors ARE polarized
“Long lead, square hole!”
Stripes face each other

## Slide 15: Attach Battery Snap
Red wire is [+]
Black wire is [‒]
Lace through center holes
Just do one at a time

## Slide 16: Time to Test!
Double check your soldering
Double check component placement
Double check component orientation
Ready?
Test it!

## Slide 17: Do Not Do It Like This

## Slide 18: Review
What did you learn?
Do you like soldering?
How to improve this class
Contact Dale Wheat
  dale@dalewheat.com
  https://www.dalewheat.com
  “dalewheat” on DMS Talk

## Slide 19: Thank You!